        Survey of the methods for voice activity detector (VAD).
    There are numerous VAD methods, but speech/non-speech detection is an unsolved problem
in speech processing, becous most of the VAD algorithms fail when the level of background
 noise increases. During the last time, numerous researchers have developed different
 strategies for detecting speech on a noisy signal.
 (Noise-Robust Voice Activity Detector Based on Hidden Semi-MarkovModels
Xianglong Liu, Yuan Liang, Yihua Lou, He Li, Baosong Shan,2010;
 Voice Activity Detection. Fundamentals and Speech Recognition System Robustness
 J. Ramírez, J. M. Górriz and J. C. Segura, 2007).
    The main idea of VAD methods is rather simple.
    The original analogue signal, which to be used by the system is converted from analogue
to discrete – s(n), 1 <= n <= N.
     When beginning the calculation and estimation of the signal it is useful to do some assumptions.
     First we needed to divide the signal into blocks(frames). The length of each block is needed to be 20ms according to the stationary properties of the signal . When using the Fs at 16 kHz, it will give us a block length of 320 samples(L=320). Consider the first 10 blocks to be background noise, then mean and variance could be calculated and used as a reference to the rest of the blocks to detect where a threshold is reached.
    Ordinarily, short-term energy and zero-crossing rate can be combined to form appropriate features for determining the onset and termination of speech boundaries. These temporal features can be extracted simply from the sample values of speech signal.

       Short-term energy is the principal and most natural feature, that has been used. This is especially to distinguish between voiced sounds and unvoiced sounds or silence, compared the performances of the following three short-term energy measurements in endpoint detection. It is observed that short-term energy is the most effective energy parameter for this task. Equation represents the squared short-Term Energy:

E(m) = sum from{n = m * L-1} to{m*L} s (n)^2 ,1<=m< N/L.
      Next is also the short-term power esimate:

P(m)= 1/L*E(m) .
     And the short-term zero-crossing rate:
Z(m)=1 over L sum from n=m*L-1 to m*l {abs{ sng(s(n))-sng(s(n-1))}over 2} .
    Where , sng(x) = -1, if x<0, and , sng(x) = 1, if x>0 .
    The short-term zero-crossing rate gives a measure of how many times the signal, s(n), changes sing.
    The squared short-term energy is most suitable. For simplicity the frame (block of fixed number of sample) processing used in speech recognition. Instead of calculating this parameter with respect to sample, calculations are done on frame basis.The short-term energy estimate will increase when speech is present in signal.
    The number of zero-crossings is also a useful temporal feature in speech analysis. It refers to the number of times speech samples change sign in a given frame. The rate at which zero-crossings occur is a simple measure of the frequency content of a narrowband signal. Zero-crossing rate is a measure of number of times in a given time interval/frame that the amplitude of the speech signals passes through a value of zero. It tends to be lager during unvoiced regions.
    These measurements need some triggers for making decision about, where the utterance begins ,and, where to end .To create a trigger one need some information about the background noise. This is done by using following procedure ;
1)Assuming that first ten blocks are background noise. With this assumption the mean and
variance for the measures are calculated. To make a more comfortable approach following function is used:
        W(m)=P(m)*(1-Z(m))*S .

        Where S is scale factor for avoiding small values, in typical application it is 1000 or more.
        2)The trigger can be described as:
t_W=%mu_W + %alpha*%delta_W

The %mu_W is mean and the %delta_W is variance for W(m) , calculated for first ten blocks.
 The term %alpha is constant, that have to be fine tuned according to the characteristics of signal.
3) The voice activation detection function is found as :
VAD(m)={left lbrace {stack{1,W(m)>=t_W#0,W(m)<=t_W}}right none} .

VAD(n) is found as VAD(m) in the block of measure.